## Slide 1: Chapter 2 Application Layer
Computer Networking: A Top Down Approach
6th edition
Jim Kurose, Keith Ross Addison-Wesley March 2012
A note on the use of these ppt slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs.
They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source
(after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2012
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 2: Chapter 2: outline
  principles of network applications
  Web and HTTP
  FTP
  electronic mail
 SMTP, POP3, IMAP
  DNS
  P2P applications
  socket programming with UDP and TCP

## Slide 3: Chapter 2: application layer
our goals:

conceptual, implementation aspects of network application protocols
transport-layer service models
client-server paradigm
peer-to-peer paradigm

learn about protocols by examining popular application-level protocols
HTTP
FTP
SMTP / POP3 / IMAP
DNS
creating network applications
socket API


## Slide 4: Some network apps







e-mail web
text messaging
remote login P2P file sharing
multi-user network games
streaming stored video (YouTube, Hulu, Netflix)


voice over IP (e.g., Skype)
real-time video conferencing
social networking search
…
…





## Slide 5: Creating a network app
write programs that:



run on (different) end systems
communicate over network
e.g., web server software communicates with browser software
no need to write software for network-core devices

network-core devices do not run user applications
applications on end systems allows for rapid app development, propagation

application | 
 | transport
 | network
 | data link
 | physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 6: Application architectures
possible structure of applications:
client-server
peer-to-peer (P2P)

## Slide 7: Client-server architecture
server:



always-on host permanent IP address data centers for scaling
clients:


communicate with server
may be intermittently connected
may have dynamic IP addresses
do not communicate directly with each other


client/server

## Slide 8: P2P architecture


no always-on server
arbitrary end systems directly communicate
peers request service from other peers, provide service in return to other peers
self scalability – new peers bring new service capacity, as well as new service demands
peers are intermittently connected and change IP addresses
complex management


peer-peer

## Slide 9: Processes communicating
process: program running within a host

within same host, two processes communicate using inter-process communication (defined by OS)
processes in different hosts communicate by exchanging messages

clients, servers
client process: process that initiates communication server process: process that
waits to be contacted
 aside: applications with P2P architectures have client processes & server processes

## Slide 10: Sockets


process sends/receives messages to/from its socket socket analogous to door
sending process shoves message out door
sending process relies on transport infrastructure on other side of door to deliver message to socket at receiving process
Internet
controlled by OS
controlled by app developer
transport
physical
link
network
application
process
transport
physical
link
network
application
process
socket

## Slide 11: Addressing processes

to receive messages, process must have identifier
host device has unique 32- bit IP address
Q: does IP address of host on which process runs suffice for identifying the process?
 A: no, many processes can be running on same host



identifier includes both IP address and port numbers associated with process on host.
example port numbers:
HTTP server: 80
mail server: 25
to send HTTP message to gaia.cs.umass.edu web server:
 IP address: 128.119.245.12
port number: 80
more shortly…




## Slide 12: App-layer protocol defines

types of messages exchanged,
e.g., request, response message syntax:
what fields in messages & how fields are delineated
message semantics
meaning of information in fields
rules for when and how processes send & respond to messages







open protocols: defined in RFCs
allows for interoperability e.g., HTTP, SMTP
proprietary protocols:
e.g., Skype

## Slide 13: What transport service does an app need?
data integrity

some apps (e.g., file transfer, web transactions) require 100% reliable data transfer
other apps (e.g., audio) can tolerate some loss

timing

some apps (e.g., Internet telephony, interactive games) require low delay to be “effective”
throughput
some apps (e.g., multimedia) require minimum amount of throughput to be “effective”
other apps (“elastic apps”) make use of whatever throughput they get
security
 encryption, data integrity,
…

## Slide 14: Transport service requirements: common apps
application
file transfer
e-mail
Web documents
interactive games text messaging
data loss
no loss
no loss
no loss
real-time audio/video loss-tolerant
loss-tolerant no loss
throughput
elastic elastic
video:10kbps-5Mbps
stored audio/video loss-tolerant same as above
few kbps up elastic
time sensitive
no
no
elastic no
audio: 5kbps-1Mbps yes, 100’s msec
yes, few secs
yes, 100’s msec yes and no

## Slide 15: Internet transport protocols services

reliable transport between sending and receiving process
flow control: sender won’t overwhelm receiver
congestion control: throttle sender when network overloaded
does not provide: timing, minimum throughput guarantee, security
connection-oriented: setup required between client and server processes
TCP service: UDP service:





unreliable data transfer between sending and receiving process
does not provide: reliability, flow control, congestion control, timing, throughput guarantee, security, orconnection setup,

Q: why bother? Why is there a UDP?

## Slide 16: Internet apps: application, transport protocols
application
e-mail
remote terminal access
Web
file transfer
streaming multimedia
Internet telephony
application layer protocol
SMTP [RFC 2821]
Telnet [RFC 854]
HTTP [RFC 2616]
FTP [RFC 959]
HTTP (e.g., YouTube), RTP [RFC 1889]
SIP, RTP, proprietary (e.g., Skype)
underlying transport protocol
TCP
TCP
TCP
TCP
TCP or UDP
TCP or UDP

## Slide 17: Securing TCP
TCP & UDP
no encryption
cleartext passwds sent into socket traverse Internet in cleartext
SSL
provides encrypted TCP connection
data integrity
end-point authentication
SSL is at app layer
Apps use SSL libraries, which “talk” to TCP
SSL socket API
cleartext passwds sent into socket traverse Internet encrypted
See Chapter 7

## Slide 18: Chapter 2: outline
  principles of network applications
    app architectures
    app requirements
  Web and HTTP
  FTP
  electronic mail
    SMTP, POP3, IMAP
  DNS
  P2P applications
  socket programming with UDP and TCP

## Slide 19: Web and HTTP
First, a review…
web page consists of objects
object can be HTML file, JPEG image, Java applet, audio file,…
web page consists of base HTML-file which includes several referenced objects
each object is addressable by a URL, e.g.,
www.someschool.edu/someDept/pic.gif
host name
path name

## Slide 20: HTTP overview
HTTP: hypertext transfer protocol

Web’s application layer protocol
client/server model
client: browser that requests, receives, (using HTTP protocol) and “displays” Web objects
server: Web server sends (using HTTP protocol) objects in response to requests

PC running Firefox browser
server running Apache Web server
iphone running Safari browser
HTTP request
HTTP response
HTTP request
HTTP response

## Slide 21: HTTP overview (continued)

client initiates TCP connection (creates socket) to server, port 80
server accepts TCP connection from client
HTTP messages (application-layer protocol messages) exchanged between browser (HTTP client) and Web server (HTTP server)
TCP connection closed
uses TCP: HTTP is “stateless”




server maintains no information about past client requests
protocols that maintain
“state” are complex!
past history (state) must be maintained
if server/client crashes, their views of “state” may be inconsistent, must be reconciled
aside

## Slide 22: HTTP connections
non-persistent HTTP
at most one object sent over TCP connection
 connection then closed
downloading multiple objects required multiple connections
persistent HTTP
 multiple objects can be sent over single TCP connection between client, server

## Slide 23: Non-persistent HTTP
suppose user enters URL:
www.someSchool.edu/someDepartment/home.index
1a. HTTP client initiates TCP connection to HTTP server (process) at www.someSchool.edu on port 80
2. HTTP client sends HTTP request message (containing URL) into TCP connection socket. Message indicates that client wants object someDepartment/home.index
1b. HTTP server at host www.someSchool.edu waiting for TCP connection at port 80. “accepts” connection, notifying client
3. HTTP server receives request message, forms response message containing requested object, and sends message into its socket
time
(contains text, references to 10 jpeg images)

## Slide 24: Non-persistent HTTP (cont.)
HTTP server closes TCP connection.
HTTP client receives response
message containing html file, displays html. Parsing html file, finds 10 referenced jpeg objects
6. Steps 1-5 repeated for each of 10 jpeg objects
time

## Slide 25: Non-persistent HTTP: response time
RTT (definition): time for a small packet to travel from client to server and back
HTTP response time:

one RTT to initiate TCP connection
one RTT for HTTP request and first few bytes of HTTP response to return
file transmission time
non-persistent HTTP response time =
2RTT+ file transmission time



time to transmit file
initiate TCP
connection
RTT
request
file
RTT
file
received
time
time

## Slide 26: Persistent HTTP
non-persistent HTTP issues:


requires 2 RTTs per object
OS overhead for each TCP connection
browsers often open parallel TCP connections to fetch referenced objects





persistent HTTP:
server leaves connection open after sending response
subsequent HTTP messages between same client/server sent over open connection
client sends requests as soon as it encounters a referenced object
as little as one RTT for all the referenced objects

## Slide 27: HTTP request message


request line (GET, POST,
carriage return, line feed at start of line indicates
end of header lines
GET /index.html HTTP/1.1\r\n
HEAD commands) Host: www-net.cs.umass.edu\r\n
User-Agent: Firefox/3.6.10\r\n
headerAccept: text/html,application/xhtml+xml\r\n
linesAccept-Language: en-us,en;q=0.5\r\n Accept-Encoding: gzip,deflate\r\n
Accept-Charset: ISO-8859-1,utf-8;q=0.7\r\n Keep-Alive: 115\r\n
Connection: keep-alive\r\n
\r\n
two types of HTTP messages: request, response
HTTP request message:
 ASCII (human-readable format)
carriage return character
line-feed character

## Slide 28: HTTP request message: general format
equest
r l
ine
header lines
body
method
cr lf
rsion
sp URL sp ve
cr
lf
value
h
eader field name
cr
lf
v
alue
h
eader field name
~
~
cr
lf
entity body
~
~

## Slide 29: Uploading form input
POST method:

web page often includes form input
input is uploaded to server in entity body

URL method:


uses GET method
input is uploaded in URL field of request line:
www.somesite.com/animalsearch?monkeys&banana

## Slide 30: Method types
HTTP/1.0:



GET POST HEAD
 asks server to leave requested object out of response
HTTP/1.1:


GET, POST, HEAD PUT
uploads file in entity body to path specified in URL field
DELETE
deletes file specified in the URL field


## Slide 31: HTTP response message
status line (protocol status code status phrase)
header
lines
data, e.g., requested HTML file
HTTP/1.1 200 OK\r\n
Date: Sun, 26 Sep 2010 20:09:20 GMT\r\n Server: Apache/2.0.52 (CentOS)\r\n
Last-Modified: Tue, 30 Oct 2007 17:00:02
GMT\r\n
ETag: "17dc6-a5c-bf716880"\r\n Accept-Ranges: bytes\r\n Content-Length: 2652\r\n
Keep-Alive: timeout=10, max=100\r\n Connection: Keep-Alive\r\n
Content-Type: text/html; charset=ISO-8859- 1\r\n
\r\n
data data data data data ...

## Slide 32: HTTP response status codes
status code appears in 1st line in server-to- client response message.
some sample codes:
200 OK
 request succeeded, requested object later in this msg
301 Moved Permanently
 requested object moved, new location specified later in this msg (Location:)
400 Bad Request
 request msg not understood by server
404 Not Found
 requested document not found on this server
505 HTTP Version Not Supported

## Slide 33: Trying out HTTP (client side) for yourself
1. Telnet to your favorite Web server:
opens TCP connection to port 80
(default HTTP server port) at cis.poly.edu. anything typed in sent
to port 80 at cis.poly.edu
telnet cis.poly.edu 80
2. type in a GET HTTP request:
GET /~ross/ HTTP/1.1 Host: cis.poly.edu
by typing this in (hit carriage return twice), you send
this minimal (but complete)
GET request to HTTP server
3. look at response message sent by HTTP server!
(or use Wireshark to look at captured HTTP request/response)

## Slide 34: User-server state: cookies
many Web sites use cookies
four components:
cookie header line of HTTP response message
cookie header line in next HTTP request message
cookie file kept on user’s host, managed by user’s browser
back-end database at Web site
example:

Susan always access Internet from PC
visits specific e-commerce site for first time
when initial HTTP requests arrives at site, site creates:
unique ID
entry in backend database for ID



## Slide 35: Cookies: keeping “state” (cont.)
client
server
usual http response msg
usual http response msg
cookie file
one week later:
usual http request msg
cookie: 1678
cookie- specific action
access
ebay 8734
usual http request msg
Amazon server creates ID 1678 for user
create
usual http response
set-cookie: 1678
ebay 8734
amazon 1678
usual http request msg
cookie: 1678
cookie- specific action
access
ebay 8734
amazon 1678
backend
entry database

## Slide 36: Cookies (continued)
what cookies can be used for:




authorization shopping carts recommendations
user session state (Web e-mail)
cookies permit sites to learn a lot about you
you may supply name and e-mail to sites
cookies and privacy: aside
how to keep “state”:
protocol endpoints: maintain state at sender/receiver over multiple transactions
cookies: http messages carry state

## Slide 37: Web caches (proxy server)

user sets browser: Web accesses via cache
browser sends all HTTP requests to cache
object in cache: cache returns object
else cache requests object from origin server, then returns object to client

goal: satisfy client request without involving origin server
client
proxy server
client
HTTP request
HTTP response
HTTP request
origin server
origin server
HTTP response
HTTP request
HTTP response

## Slide 38: More about Web caching
cache acts as both client and server
  server for original requesting client
  client to origin server
typically cache is installed by ISP (university, company, residential ISP)
why Web caching?
reduce response time for client request
reduce traffic on an institution’s access link
Internet dense with caches: enables “poor” content providers to effectively deliver content (so too does P2P file sharing)

## Slide 39: Caching example:
origin servers
public Internet
institutional network
1 Gbps LAN
1.54 Mbps access link
assumptions:
avg object size: 100K bits
avg request rate from browsers to origin servers:15/sec
avg data rate to browsers: 1.50 Mbps
RTT from institutional router to any origin server: 2 sec
access link rate: 1.54 Mbps
consequences:
 LAN utilization: 15%
 access link utilization = 99%
 total delay = Internet delay + access delay + LAN delay
= 2 sec + minutes + usecs
problem!

## Slide 40: Caching example: fatter access link



total delay = Internet delay + access delay + LAN delay
origin servers
1.54 Mbps
access link
assumptions:
avg object size: 100K bits
avg request rate from browsers to origin servers:15/sec
avg data rate to browsers: 1.50 Mbps
RTT from institutional router to any origin server: 2 sec
access link rate: 1.54 Mbps154 Mbps
consequences:
154 Mbps
= 2 sec + minutes + usecs
msecs
Cost: increased access link speed (not cheap!)
LAN utilization: 15%
access link utilization = 99%9.9%
public Internet
institutional network
1 Gbps LAN

## Slide 41: Caching example: install local cache
institutional network
1 Gbps LAN
origin servers
1.54 Mbps access link
local web cache
assumptions:
avg object size: 100K bits
avg request rate from browsers to origin servers:15/sec
avg data rate to browsers: 1.50 Mbps
RTT from institutional router to any origin server: 2 sec
access link rate: 1.54 Mbps
consequences:



LAN utilization: 15%
access link utilization?= 100%
total delay ?= Internet delay + access
delayH+owLANtodceolamy pute link
= 2 secu+tilmizianutitoens ,+dueselacys ?
public Internet
Cost: web cache (cheap!)

## Slide 42: Caching example: install local cache
Calculating access link utilization, delay with cache:
 suppose cache hit rate is 0.4
 40% requests satisfied at cache, 60% requests satisfied at origin
access link utilization:
origin servers
1.54 Mbps access link

60% of requests use access link
 data rate to browsers over access link
= 0.6*1.50 Mbps = .9 Mbps

utilization = 0.9/1.54 = .58
total delay

= 0.6 * (delay from origin servers) +0.4
* (delay when satisfied at cache)
= 0.6 (2.01) + 0.4 (~msecs)
= ~ 1.2 secs
less than with 154 Mbps link (and cheaper too!)



public Internet
institutional network
1 Gbps LAN
local web cache
Application Layer 2-42

## Slide 43: Conditional GET

Goal: don’t send object if cache has up-to-date cached version
no object transmission delay
lower link utilization
cache: specify date of cached copy in HTTP request
If-modified-since:
<date>
server: response contains no object if cached copy is up-to-date:
HTTP/1.0 304 Not
Modified


HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0
304 Not Modified
object not modified before
<date>
HTTP request msg
If-modified-since: <date>
HTTP response
HTTP/1.0 200 OK
<data>
object modified after
<date>
client
server

## Slide 44: Chapter 2: outline
  principles of network applications
    app architectures
    app requirements
  Web and HTTP
  FTP
  electronic mail
    SMTP, POP3, IMAP
  DNS
  P2P applications
  socket programming with UDP and TCP

## Slide 45: FTP: the file transfer protocol
file transfer
FTP
server
FTP
user interface
FTP
client
local file system
remote file system
user at host
transfer file to/from remote host
client/server model
  client: side that initiates transfer (either to/from remote)
  server: remote host
ftp: RFC 959
ftp server: port 21

## Slide 46: FTP: separate control, data connections

FTP client contacts FTP server at port 21, using TCP
client authorized over control connection
client browses remote directory, sends commands over control connection
when server receives file transfer command, server opens 2nd TCP data connection (for file) to client
after transferring one file, server closes data connection




FTP
client
FTP
server
TCP control connection, server port 21
TCP data connection,
server port 20
server opens another TCP data connection to transfer another file
control connection: “out of band”
FTP server maintains “state”: current directory, earlier authentication

## Slide 47: FTP commands, responses

sent as ASCII text over control channel
USER username
PASS password
LIST return list of file in current directory
RETR filename
retrieves (gets) file
STOR filename stores (puts) file onto remote host
sample commands: sample return codes






status code and phrase (as in HTTP)
331 Username OK, password required
125 data connection already open; transfer starting
425 Can’t open data connection
452 Error writing file





## Slide 48: Chapter 2: outline
  principles of network applications
    app architectures
    app requirements
  Web and HTTP
  FTP
  electronic mail
    SMTP, POP3, IMAP
  DNS
  P2P applications
  socket programming with UDP and TCP

## Slide 49: Electronic mail
Three major components:



user agents mail servers
simple mail transfer protocol: SMTP
User Agent


a.k.a. “mail reader”
composing, editing, reading mail messages
e.g., Outlook, Thunderbird, iPhone mail client
outgoing, incoming messages stored on server


outgoing message queue
user mailbox
mail
server
mail
server
mail
server
SMTP
SMTP
SMTP
user agent
user agent
user agent
user agent
user agent
user agent

## Slide 50: Electronic mail: mail servers
mail servers:

mailbox contains incoming messages for user
message queue of outgoing (to be sent) mail messages
SMTP protocol between mail servers to send email messages
client: sending mail server
“server”: receiving mail server


mail server
mail
server
mail
server
SMTP
SMTP
SMTP
user agent
user agent
user agent
user agent
user agent
user agent

## Slide 51: Electronic Mail: SMTP [RFC 2821]
uses TCP to reliably transfer email message from client to server, port 25
direct transfer: sending server to receiving server
three phases of transfer
  handshaking (greeting)
  transfer of messages
  closure
command/response interaction (like HTTP, FTP)
  commands: ASCII text
  response: status code and phrase
messages must be in 7-bit ASCI

## Slide 52: Scenario: Alice sends message to Bob
agent
Alice uses UA to compose message “to” bob@someschool.edu
Alice’s UA sends message to her mail server; message placed in message queue
client side of SMTP opens TCP connection with Bob’s mail server
SMTP client sends Alice’s message over the TCP connection
Bob’s mail server places the message in Bob’s mailbox
Bob invokes his user agent to read message
mail server
mail
server
1 user
2
3
4
6
Alice’s mail server
5
Bob’s mail server
user agent

## Slide 53: Sample SMTP interaction
S: 220 hamburger.edu C: HELO crepes.fr
S: 250 Hello crepes.fr, pleased to meet you C: MAIL FROM: <alice@crepes.fr>
S: 250 alice@crepes.fr... Sender ok C: RCPT TO: <bob@hamburger.edu>
S: 250 bob@hamburger.edu ... Recipient ok C: DATA
S: 354 Enter mail, end with "." on a line by itself C: Do you like ketchup?
C: How about pickles? C: .
S: 250 Message accepted for delivery C: QUIT
S: 221 hamburger.edu closing connection

## Slide 54: Try SMTP interaction for yourself:



telnet servername 25
see 220 reply from server
enter HELO, MAIL FROM, RCPT TO, DATA, QUIT
commands
above lets you send email without using email client (reader)

## Slide 55: SMTP: final words

SMTP uses persistent connections
SMTP requires message (header & body) to be in 7-bit ASCII
SMTP server uses
CRLF.CRLF to
determine end of message







comparison with HTTP:
HTTP: pull SMTP: push
both have ASCII command/response interaction, status codes
HTTP: each object encapsulated in its own response msg
SMTP: multiple objects sent in multipart msg

## Slide 56: Mail message format
SMTP: protocol for exchanging email msgs
RFC 822: standard for text message format:

header lines, e.g.,
To:
From:
Subject:
different from SMTP MAIL FROM, RCPT TO:
commands!
Body: the “message”
 ASCII characters only

header
body
blank line

## Slide 57: Mail access protocols


SMTP: delivery/storage to receiver’s server mail access protocol: retrieval from server
POP: Post Office Protocol [RFC 1939]: authorization, download
IMAP: Internet Mail Access Protocol [RFC 1730]: more features, including manipulation of stored msgs on server
HTTP: gmail, Hotmail, Yahoo! Mail, etc.
sender’s mail server
SMTP
SMTP
mail access
protocol
receiver’s mail server
(e.g., POP,
IMAP)
user agent
user agent

## Slide 58: POP3 protocol
authorization phase

client commands:
user: declare username
pass: password server responses
 +OK
-ERR

transaction phase, client:


list: list message numbers
retr: retrieve message by number
dele: delete
quit


S: +OK POP3 server ready C: user bob
S: +OK
C: pass hungry
S: +OK user successfully logged on
C: list S: 1 498
S: 2 912 S: .
C: retr 1
S: <message 1 contents> S: .
C: dele 1
C: retr 2
S: <message 1 contents> S: .
C: dele 2 C: quit
S: +OK POP3 server signing off

## Slide 59: POP3 (more) and IMAP
more about POP3

previous example uses POP3 “download and delete” mode
 Bob cannot re-read e- mail if he changes client
POP3 “download-and- keep”: copies of messages on different clients
POP3 is stateless across sessions


IMAP

keeps all messages in one place: at server
allows user to organize messages in folders
keeps user state across sessions:
 names of folders and mappings between message IDs and folder name



## Slide 60: Chapter 2: outline
  principles of network applications
    app architectures
    app requirements
  Web and HTTP
  FTP
  electronic mail
    SMTP, POP3, IMAP
  DNS
  P2P applications
  socket programming with UDP and TCP

## Slide 61: DNS: domain name system
people: many identifiers:
SSN, name, passport #
Internet hosts, routers:
IP address (32 bit) - used for addressing datagrams
“name”, e.g., www.yahoo.com - used by humans
Q: how to map between IP address and name, and vice versa ?


Domain Name System:
distributed database implemented in hierarchy of many name servers
application-layer protocol: hosts, name servers communicate to resolve names (address/name translation)
note: core Internet function, implemented as application- layer protocol
complexity at network’s “edge”

## Slide 62: DNS: services, structure




why not centralize DNS? single point of failure traffic volume
distant centralized database maintenance
A: doesn’t scale!
DNS services

hostname to IP address translation
host aliasing
canonical, alias names
mail server aliasing load distribution
replicated Web servers: many IP addresses correspond to one name




## Slide 63: DNS: a distributed, hierarchical database
com DNS servers
org DNS servers edu DNS servers
Root DNS Servers
… …
poly.edu umass.edu DNS serversDNS servers
yahoo.com DNS servers
amazon.com DNS servers
pbs.org DNS servers
client wants IP for www.amazon.com; 1st approx:



client queries root server to find com DNS server
client queries .com DNS server to get amazon.com DNS server
client queries amazon.com DNS server to get IP address for www.amazon.com

## Slide 64: DNS: root name servers


contacted by local name server that can not resolve name root name server:
contacts authoritative name server if name mapping not known
gets mapping
returns mapping to local name server
13 root name “servers” worldwide
e. NASA Mt View, CA
f. Internet Software C.
Palo Alto, CA (and 48 other sites)
i. Netnod, Stockholm (37 other sites)
k. RIPE London (17 other sites)
m. WIDE Tokyo (5 other sites)
c. Cogent, Herndon, VA (5 other sites)
d. U Maryland College Park, MD
h. ARL Aberdeen, MD
j. Verisign, Dulles VA (69 other sites )
Verisign, Los Angeles CA (5 other sites)
USC-ISI Marina del Rey, CA
l. ICANN Los Angeles, CA (41 other sites)
g. US DoD Columbus,
OH (5 other sites)

## Slide 65: TLD, authoritative servers
top-level domain (TLD) servers:
responsible for com, org, net, edu, aero, jobs, museums, and all top-level country domains, e.g.: uk, fr, ca, jp
Network Solutions maintains servers for .com TLD
Educause for .edu TLD
authoritative DNS servers:
organization’s own DNS server(s), providing authoritative hostname to IP mappings for organization’s named hosts
can be maintained by organization or service provider

## Slide 66: Local DNS name server
does not strictly belong to hierarchy
each ISP (residential ISP, company, university) has one
  also called “default name server”
when host makes DNS query, query is sent to its local DNS server
  has local cache of recent name-to-address translation pairs (but may be out of date!)
  acts as proxy, forwards query into hierarchy

## Slide 67: DNS name resolution example
requesting host
cis.poly.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.poly.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server

host at cis.poly.edu wants IP address for gaia.cs.umass.edu
iterated query:
contacted server replies with name of server to contact
“I don’t know this name, but ask this server”

## Slide 68
DNS name resolution Iteration Cont..
As shown in Figure , the host cis.poly.edu first sends a DNS query message to its local DNS server, dns.poly.edu. The query message contains the hostname to be translated, namely, gaia.cs.umass.edu. The local DNS server forwards the query message to a root DNS server. The root DNS server takes note of the edu suffix and returns to the local DNS server a list of IP addresses for TLD servers responsible for edu. The local DNS server then resends the query message to one of these TLD servers. The TLD server takes note of the umass.edu suffix and responds with the IP address of the authoritative DNS server for the University of Massachusetts, namely, dns.umass.edu. Finally, the local DNS server resends the query message directly to dns.umass.edu, which responds with the IP address of gaia.cs.umass.edu. Note that in this example, in order to obtain the mapping for one hostname, eight DNS messages were sent: four query messages and four reply messages

## Slide 69: DNS name resolution example
4
5
6
3
recursive query:
 puts burden of name resolution on
contacted name server
 heavy load at upper levels of hierarchy?
requesting host
cis.poly.edu
gaia.cs.umass.edu
root DNS server
2
7
local DNS server
dns.poly.edu
1 8
authoritative DNS server
dns.cs.umass.edu
TLD DNS
server

## Slide 70: DNS name resolution example
4
5
6
3
recursive query:
A recursive DNS lookup is where one DNS server communicates with several other DNS servers to hunt down an IP address and return it to the client. This is in contrast to an iterative DNS query, where the client communicates directly with each DNS server involved in the lookup.
requesting host
cis.poly.edu
gaia.cs.umass.edu
root DNS server
2
7
local DNS server
dns.poly.edu
1 8
authoritative DNS server
dns.cs.umass.edu
TLD DNS
server

## Slide 71: DNS: caching, updating records
once (any) name server learns mapping, it caches
mapping
  cache entries timeout (disappear) after some time (TTL)
  TLD servers typically cached in local name servers
    thus root name servers not often visited
cached entries may be out-of-date (best effort name-to-address translation!)
  if name host changes IP address, may not be known Internet-wide until all TTLs expire
update/notify mechanisms proposed IETF standard
 RFC 2136

## Slide 72: DNS records
DNS: distributed db storing resource records (RR)
type=NS
name is domain (e.g., foo.com)
value is hostname of authoritative name server for this domain
RR format: (name, value, type, ttl)
type=A


name is hostname
value is IP address
type=CNAME

name is alias name for some “canonical” (the real) name
www.ibm.com is really
servereast.backup2.ibm.com
value is canonical name


type=MX

value is name of mailserver associated with name

## Slide 73: DNS protocol, messages
 query and reply messages, both with same message
format
msg header
identification: 16 bit # for query, reply to query uses same #
flags:




query or reply recursion desired recursion available reply is authoritative
identification
flags
questions (variable # of questions)
# authority RRs # additional RRs
# questions #
answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
2 bytes 2 bytes

## Slide 74: DNS protocol, messages
name, type fields
for a query
RRs in response
to query
records for authoritative servers
additional “helpful” info that may be used
identification
flags
questions (variable # of questions)
# authority RRs # additional RRs
# questions #
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
a
dditional info (variable # of RRs)
2 bytes
2 bytes

## Slide 75: Inserting records into DNS
example: new startup “Network Utopia”
register name networkuptopia.com at DNS registrar
(e.g., Network Solutions)
  provide names, IP addresses of authoritative name server (primary and secondary)
  registrar inserts two RRs into .com TLD server: (networkutopia.com, dns1.networkutopia.com, NS) (dns1.networkutopia.com, 212.212.212.1, A)
create authoritative server type A record for www.networkuptopia.com; type MX record for networkutopia.com

## Slide 76: Attacking DNS
DDoS attacks
Bombard root servers with traffic
  Not successful to date
  Traffic Filtering
  Local DNS servers cache IPs of TLD servers, allowing root server bypass
Bombard TLD servers
  Potentially more dangerous
Redirect attacks
Man-in-middle
  Intercept queries
DNS poisoning
  Send bogus relies to DNS server, which caches
Exploit DNS for DDoS
Send queries with spoofed source address: target IP
Requires amplification

## Slide 77: Chapter 2: outline
  principles of network applications
    app architectures
    app requirements
  Web and HTTP
  FTP
  electronic mail
    SMTP, POP3, IMAP
  DNS
  P2P applications
  socket programming with UDP and TCP

## Slide 78: Pure P2P architecture


no always-on server
arbitrary end systems directly communicate
peers are intermittently connected and change IP addresses

examples:
file distribution (BitTorrent)
Streaming (KanKan)
VoIP (Skype)

## Slide 79: File distribution: client-server vs P2P
Question: how much time to distribute file (size F) from one server to N peers?
 peer upload/download capacity is limited resource
us
uN
dN
server
network (with abundant bandwidth)
file, size F
us: server upload capacity
ui: peer i upload capacity
di: peer i download capacity
u2
d
2
u
1
d1
di
ui

## Slide 80: File distribution time: client-server

server transmission: must sequentially send (upload) N file copies:


time to send one copy: F/u
s
time to send N copies: NF/us
increases linearly in N
time to distribute F
to N clients usDing
client-server approac c-s
h
s,
min
> max{NF/u ,F/d }
 client: each client must download file copy


dmin = min client download rate min client download time: F/dmin
us
network
di
ui
F

## Slide 81: File distribution time: P2P

server transmission: must upload at least one copy

time to send one copy: F/us
time to distribute F to N clients usiDng
us
network
d
i
ui
F
P2P
> max{F/us,,F/dmin,,NF/(us + ui)}
 client: each client must download file copy

min client download time: F/dmin
P2P approach
increases linearly in N …
… but so does this, as each peer brings service capacity
 clients: as aggregate must download NF bits

max upload rate (limting max download rate) is us + ui

## Slide 82: Client-server vs. P2P: example
2.5
2
1.5
1
0.5
0
3
3.5
0
5
10
15
20
25
30
35
N
Minimum Distribution Time
P2P
Client-Server
client upload rate = u, F/u = 1 hour, us = 10u, dmin ≥ us

## Slide 83: P2P file distribution: BitTorrent
tracker: tracks peers participating in torrent
torrent: group of peers exchanging chunks of a file
Alice arrives …
… obtains list
of peers from tracker
… and begins exchanging
file chunks with peers in torrent
file divided into 256Kb chunks
peers in torrent send/receive file chunks

## Slide 84: P2P file distribution: BitTorrent

peer joining torrent:
has no chunks, but will accumulate them over time from other peers
registers with tracker to get list of peers, connects to subset of peers (“neighbors”)
while downloading, peer uploads chunks to other peers
peer may change peers with whom it exchanges chunks
churn: peers may come and go
once peer has entire file, it may (selfishly) leave or (altruistically) remain in torrent

## Slide 85: BitTorrent: requesting, sending file chunks
requesting chunks:

at any given time, different peers have different subsets of file chunks
periodically, Alice asks each peer for list of chunks that they have
Alice requests missing chunks from peers, rarest first






sending chunks: tit-for-tat
Alice sends chunks to those four peers currently sending her chunks at highest rate
other peers are choked by Alice (do not receive chunks from her)
re-evaluate top 4 every10 secs
every 30 secs: randomly select another peer, starts sending chunks
“optimistically unchoke” this peer newly chosen peer may join top 4

## Slide 86: BitTorrent: tit-for-tat
Alice “optimistically unchokes” Bob
Alice becomes one of Bob’s top-four providers; Bob reciprocates
Bob becomes one of Alice’s top-four providers
higher upload rate: find better trading partners, get file faster !

## Slide 87: Distributed Hash Table (DHT)
Hash table
DHT paradigm
Circular DHT and overlay networks
Peer churn

## Slide 88: Simple Database
Key | Value
John Washington | 132-54-3570
Diana Louise Jones | 761-55-3791
Xiaoming Liu | 385-41-0902
Rakesh Gopal | 441-89-1956
Linda Cohen | 217-66-5609
……. | ………
Lisa Kobayashi | 177-23-0199
Simple database with(key, value) pairs:
key: human name; value: social security #
key: movie title; value: IP address

## Slide 89: Hash Table
Original Key | Key | Value
John Washington | 8962458 | 132-54-3570
Diana Louise Jones | 7800356 | 761-55-3791
Xiaoming Liu | 1567109 | 385-41-0902
Rakesh Gopal | 2360012 | 441-89-1956
Linda Cohen | 5430938 | 217-66-5609
……. |  | ………
Lisa Kobayashi | 9290124 | 177-23-0199
More convenient to store and search on numerical representation of key
key = hash(original key)

## Slide 90: Distributed Hash Table (DHT)
Distribute (key, value) pairs over millions of peers
  pairs are evenly distributed over peers
Any peer can query database with a key
  database returns value for the key
  To resolve query, small number of messages exchanged among peers
Each peer only knows about a small number of other peers
Robust to peers coming and going (churn)

## Slide 91: Assign key-value pairs to peers
rule: assign key-value pair to the peer that has the
closest ID.
convention: closest is the immediate successor of the key.
 e.g., ID space {0,1,2,3,…,63}
 suppose 8 peers: 1,12,13,25,32,40,48,60
  If key = 51, then assigned to peer 60
  If key = 60, then assigned to peer 60
  If key = 61, then assigned to peer 1

## Slide 92: Circular DHT
1
12
13
25
32
40
48
60
•
each peer only aware of immediate successor and predecessor.
“overlay network”

## Slide 93: Resolving a query
1
12
13
25
32
40
48
60
What is the value associated with key 53 ?
value
O(N) messages
on avgerage to resolve query, when there
are N peers

## Slide 94: Circular DHT with shortcuts
•
each peer keeps track of IP addresses of predecessor, successor, short cuts.
reduced from 6 to 3 messages.
possible to design shortcuts with O(log N) neighbors, O(log N)
messages in query
•
•
1
12
13
25
32
40
48
60
What is the value for
key 53
value

## Slide 95: Peer churn 1
example: peer 5 abruptly leaves
3
4
5
8
10
15
12
handling peer churn:
peers may come and go (churn)
each peer knows address of its two successors
each peer periodically pings its two successors to check aliveness
if immediate successor leaves, choose next successor as new immediate successor

## Slide 96: Peer churn 1
example: peer 5 abruptly leaves
peer 4 detects peer 5’s departure; makes 8 its immediate successor
 4 asks 8 who its immediate successor is; makes 8’s immediate successor its second successor.
3
4
8
10
12
15
handling peer churn:
peers may come and go (churn)
each peer knows address of its two successors
each peer periodically pings its two successors to check aliveness
if immediate successor leaves, choose next successor as new immediate successor

## Slide 97: Chapter 2: outline
  principles of network applications
    app architectures
    app requirements
  Web and HTTP
  FTP
  electronic mail
    SMTP, POP3, IMAP
  DNS
  P2P applications
  socket programming with UDP and TCP

## Slide 98: Socket programming
goal: learn how to build client/server applications that communicate using sockets
socket: door between application process and end- end-transport protocol
Internet
controlled by OS
controlled by app developer
transport
physical
link
network
application
process
transport
physical
link
network
application
process
socket

## Slide 99: Socket programming
Two socket types for two transport services:


UDP: unreliable datagram
TCP: reliable, byte stream-oriented
Application Example:
Client reads a line of characters (data) from its keyboard and sends the data to the server.
The server receives the data and converts characters to uppercase.
The server sends the modified data to the client.
The client receives the modified data and displays the line on its screen.

## Slide 100: Socket programming with UDP
UDP: no “connection” between client & server


no handshaking before sending data
sender explicitly attaches IP destination address and port # to each packet
rcvr extracts sender IP address and port# from received packet

UDP: transmitted data may be lost or received out-of-order
Application viewpoint:

UDP provides unreliable transfer of groups of bytes (“datagrams”) between client and server

## Slide 101: Client/server socket interaction: UDP
close clientSocket
read datagram from clientSocket
create socket: clientSocket =
socket(AF_INET,SOCK_DGRAM)
Create datagram with server IP and port=x; send datagram via clientSocket
create socket, port= x: serverSocket =
socket(AF_INET,SOCK_DGRAM)
read datagram from serverSocket
write reply to serverSocket specifying client address, port number
Application 2-99
server (running on serverIP) client

## Slide 102: Example app: UDP client
from socket import * serverName = ‘hostname’ serverPort = 12000
socket.SOCK_DGRAM) message = raw_input(’Input lowercase sentence:’) clientSocket.sendto(message,(serverName, serverPort)) modifiedMessage, serverAddress =
clientSocket.recvfrom(2048) print modifiedMessage
clientSocket.close()
create UDP socket for clientSocket = socket(socket.AF_INET,
Python UDPClient
include Python’s socket
library
server
get user keyboard
input
Attach server name, port to message; send into socket
print out received string and close socket
read reply characters from socket into string
Application Layer 2-102

## Slide 103: Example app: UDP server
serverSocket = socket(AF_INET, SOCK_DGRAM) serverSocket.bind(('', serverPort))
print “The server is ready to receive” while 1:
message, clientAddress = serverSocket.recvfrom(2048) modifiedMessage = message.upper() serverSocket.sendto(modifiedMessage, clientAddress)
Python UDPServer from socket import * serverPort = 12000
create UDP socket
bind socket to local port number 12000
loop forever
Read from UDP socket into message, getting
client’s address (client IP and port)
send upper case string back to this client
Application Layer 2-103

## Slide 104: Socket programming with TCP
Application Layer 2-104
client must contact server

server process must first be running
server must have created socket (door) that welcomes client’s contact

client contacts server by:

Creating TCP socket, specifying IP address, port number of server process
when client creates socket: client TCP establishes connection to server TCP


when contacted by client, server TCP creates new socket for server process to communicate with that particular client
allows server to talk with multiple clients
source port numbers used to distinguish clients (more in Chap 3)
application viewpoint:
TCP provides reliable, in-order byte-stream transfer (“pipe”) between client and server

## Slide 105: Client/server socket interaction:TCP
wait for incoming connection request connectionSocket =
serverSocket.accept()
server (running on hostid)
create socket, port=x, for incoming request:
serverSocket = socket()
create socket,
connect to hostid, port=x clientSocket = socket()
client
send request using clientSocket
read request from connectionSocket
write reply to connectionSocket
TCP
connection setup
close connectionSocket
read reply from clientSocket
close clientSocket
Application Layer 2-105

## Slide 106: Example app: TCP client
Python TCPClient
from socket import * serverName = ’servername’
serverPort = 12000
modifiedSentence = clientSocket.recv(1024) print ‘From Server:’, modifiedSentence clientSocket.close()
No need to attach server clientSocket.send(sentence)
create TCP socket for
server, remote port 12000 clientSocket = socket(AF_INET, SOCK_STREAM)
clientSocket.connect((serverName,serverPort)) sentence = raw_input(‘Input lowercase sentence:’)
name, port
Application Layer 2-106

## Slide 107: Example app: TCP server
serverPort = 12000
serverSocket = socket(AF_INET,SOCK_STREAM) serverSocket.bind((‘’,serverPort)) serverSocket.listen(1)
print ‘The server is ready to receive’ while 1:
Python TCPServer
from socket import *
connectionSocket, addr = serverSocket.accept()
sentence = connectionSocket.recv(1024) capitalizedSentence = sentence.upper() connectionSocket.send(capitalizedSentence) connectionSocket.close()
create TCP welcoming
socket
server begins listening for incoming TCP requests
loop forever
server waits on accept()
for incoming requests, new socket created on return
read bytes from socket (but not address as in UDP)
close connection to this
client (but not welcoming socket)
Application Layer 2-107

## Slide 108: Chapter 2: summary
Application Layer 2-108

application architectures
client-server
P2P
application service requirements:
reliability, bandwidth, delay
Internet transport service model
connection-oriented, reliable:TCP
unreliable, datagrams: UDP


our study of network apps now complete!
specific protocols:
  HTTP
  FTP
  SMTP, POP, IMAP
  DNS
  P2P: BitTorrent, DHT
socket programming: TCP, UDP sockets

## Slide 109: Chapter 2: summary

typical request/reply message exchange:
client requests info or service
server responds with data, status code
message formats:
headers: fields giving info about data
data: info being communicated

important themes:
control vs. data msgs
 in-band, out-of-band
centralized vs. decentralized
stateless vs. stateful
reliable vs. unreliable msg transfer
“complexity at network edge”
Application Layer 2-109
most importantly: learned about protocols!

## Slide 110: Chapter 1 Additional Slides
Introduction 1-108

## Slide 111: application (www browser, email client)
 | application | 
 | OS | 
Transport (TCP/UDP) |  | 
Network (IP) |  | 
Link (Ethernet) |  | 
Physical |  | 
packet capture (pcap)
packet
analyzer
copy of all Ethernet
frames sent/receive d